## Slide 1: OS161

## Slide 2: MIPS
MIPS uses 32bits paged virtual and physical address
MIPS has software managed TLB
  Software TLB raises exception on every miss
  Kernel is free to record virtual to physical mapping
  TLB functions are handled by a function called vm_fault
    kern/arch/mips/vm/dumbvm.c line 146
vm_fault uses information from addrspace structure to determine virtual to physical mapping to load into the TLB
  Each process has its own addrspace structure
  Each addrspace structure describe where the pages are stored in physical memory
  addrspace does the same job as a page table, but in a much simpler way. OS161 create contiguous segment.

## Slide 3: OS161 address space
kern/include/addrspace.h
struct addrspace {
vaddr_t as_vbase1; /* base virtual address of code segment */
paddr_t as_pbase1; /* base physical address of code segment */
size_t as_npages1; /* size (in pages) of code segment */
vaddr_t as_vbase2; /* base virtual address of data segment */
paddr_t as_pbase2; /* base physical address of data segment */
size_t as_npages2; /* size (in pages) of data segment */
paddr_t as_stackpbase; /* base physical address of stack */
};
code
code
data
data
stack
stack
vbase2
vbase1
npages1
npages2
pbase1
pbase2
stackbase

## Slide 4: dumbvm Address Translation
vbase1 = as->as_vbase1;
vtop1 = vbase1 + as->as_npages1 * PAGE_SIZE;
vbase2 = as->as_vbase2;
vtop2 = vbase2 + as->as_npages2 * PAGE_SIZE;
stackbase = USERSTACK - DUMBVM_STACKPAGES * PAGE_SIZE;
stacktop = USERSTACK;
if (faultaddress >= vbase1 && faultaddress < vtop1) {
paddr = (faultaddress - vbase1) + as->as_pbase1;
} else if (faultaddress >= vbase2 && faultaddress < vtop2) {
paddr = (faultaddress - vbase2) + as->as_pbase2;
} else if (faultaddress >= stackbase && faultaddress < stacktop) {
paddr = (faultaddress - stackbase) + as->as_stackpbase;
} else {
return EFAULT;
}
USERSTACK = 0x8000 0000
DUMBVM STACKPAGES = 12
PAGE SIZE = 4KB
kern/arch/mips/vm/dumbvm.c
Line 202
Line 222 – 239 update TLB

## Slide 5: Initializing address space
When the kernel creates a process it:
  Creates an address space
  Load the program data and code
OS161 pre-load the programs in RAM
  Most OS will load on demand
A program code and data is described in an executable
OS161 uses ELF (executable link format) as other OS (e.g., LINUX)
OS161 execv system call reinitializes the address space of a process
  int execv(const char *program, char **args)
The program parameter should be the name of the ELF executable to be loaded

## Slide 6: ELF files
ELF files contain address space segment descriptions
  ELF header describes the segment images
    the virtual address of the start of the segment
    the length of the segment in the virtual address space t
    the location of the segment in the ELF
    the length of the segment in the ELF
the ELF file identifies the (virtual) address of the program’s first instruction (the entry point)
the ELF file also contains lots of other information (e.g., section descriptors, symbol tables) that is useful to compilers, linkers, debuggers, loaders and other tools used to build programs

## Slide 7: OS161
OS161’s dumbvm implementation assumes that an ELF file contains two segments
  a text segment, containing the program code any read-only data
  a data segment, containing any other global program data
the images in the ELF file are an exact copy of the binary data to be stored in the address
dumbvm creates a stack segment for each process
  12 pages long
  ending at virtual address 0x7FFFFFFF

## Slide 8: OS161
If the image is smaller than the segment it is in loaded into, it should be zero filled
Look through and understand: kern/syscall/loadelf.c

## Slide 9: Thank you