## Slide 1: Computer Systems B COMS20012
Introduction to Operating Systems and Security

## Slide 2: Swapping

## Slide 3: Swapping pages out
Physical RAM may be oversubscribed
  Total virtual pages greater than the number of physical pages
Swapping is moving virtual pages from physical RAM to a swap device
  SSD
  Hard Drive
  etc.

## Slide 4: What’s in a page table entry (Linux)
One bit to state if the memory is present in memory or not
Physical Page Info
P

## Slide 5: What’s in a page table entry (Linux)
One bit to state if the memory is present in memory or not
Physical Page Info
P
If P==0 we do not need this, use it to store swap info

## Slide 6: What’s in a page table entry (Linux)
One bit to state if the memory is present in memory or not
Kernel maintain a list of swap file
Each file contains several map
Physical Page Info
P
Index in file
File index

## Slide 7: What’s in a page table entry (Linux)
One bit to state if the memory is present in memory or not
Kernel maintain a list of swap file
Each file contains several map
This is greatly simplified, but sufficient
  Details for interested students: https://www.kernel.org/doc/gorman/html/understand/understand014.html
Physical Page Info
P
Index in file
File index

## Slide 8: Page Faults
When process try to access page not in memory, problem detected because the presence bit is set to 0
  With hardware TLB, the MMU detect this when checking the PTE and raise an exception
  With software TLB, the kernel detects the problem on TLB miss, the TLB should not contain entry for page not present in memory!
Attempting to access a page not in RAM is a page fault
The kernel job on page fault is to:
  Swap the page from secondary storage to memory, evicting another page if necessary
  Update the PTE (set physical address + presence bit)
  Return from the exception so the application can try again

## Slide 9: Page Faults are slow!
Accessing secondary storage is slow
  Millisecond for harddrive
  Microsecond for SSD
  … comparing to nanoseconds for RAM
Suppose secondary storage is 1000 time slower
  1 in 10 access results in page fault -> Average access 100 times slower
  1 in 100 access results in page fault -> Average access 10 times slower
  1 in 1000 access results in page fault -> Average access 2 times slower
Goal is to reduce occurrence of page faults
  Limit the number of processes, so that there is enough RAM
  Hide latencies by prefetching a page before a process needs them
  Be clever about which page is kept in physical memory and which page is evicted

## Slide 10: Page Faults are slow!
Accessing secondary storage is slow
  Millisecond for harddrive
  Microsecond for SSD
  … comparing to nanoseconds for RAM
Suppose secondary storage is 1000 time slower
  1 in 10 access results in page fault -> Average access 100 times slower
  1 in 100 access results in page fault -> Average access 10 times slower
  1 in 1000 access results in page fault -> Average access 2 times slower
Goal is to reduce occurrence of page faults
  Limit the number of processes, so that there is enough RAM
  Hide latencies by prefetching a page before a process needs them
  Be clever about which page is kept in physical memory and which page is evicted

## Slide 11: Simplest replacement policy: FIFO
What page to evict?
FIFO: remove the page that has been in memory the longest
Num | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Refs | a | b | c | d | a | b | e | a | b
PP1 | a | a | a | d | d | d | e | e | e
PP2 |  | b | b | b | a | a | a | a | a
PP3 |  |  | c | c | c | b | b | b | b
Fault? | x | x | x | x | x | x | x |  | 

## Slide 12: Optimum replacement policy: MIN
What page to evict?
MIN: replace the page that won’t be referenced for the longest
Num | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Refs | a | b | c | d | a | b | e | a | b
PP1 | a | a | a | a | a | a | a | a | a
PP2 |  | b | b | b | b | b | b | b | b
PP3 |  |  | c | d | d | d | e | e | e
Fault? | x | x | x | x |  |  | x |  | 

## Slide 13: Least recently used (LRU) replacement policy
What page to evict?
LRU : remove the page that has been used the least recently (temporal locality)
Num | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Refs | a | b | c | d | a | b | e | a | b
PP1 | a | a | a | d | d | d | e | e | e
PP2 |  | b | b | b | a | a | a | a | a
PP3 |  |  | c | c | c | b | b | b | b
Fault? | x | x | x | x | x | x | x |  | 

## Slide 14: Practical replacement policy: Clock
What page to evict?
Add a “used” bit to PTE
  Set by MMU when page accessed
  Can be cleared by kernel
victim = 0
while use bit of victim is set
  clear use bit of victim
  victim = (victim + 1) % num_frames
evict victim