## Slide 1: Computer Systems B COMS20012
Introduction to Operating Systems and Security

## Slide 2: Translation Lookaside Buffer

## Slide 3: Previously
Problem
  One virtual memory access
  Requires two physical memory access
    Load directory entry
    Load page entry
  Generate “real” memory access
directory #
offset
Virtual Address
page #
page #
offset
Physical Address
directory entry
directory entry
directory entry
directory entry
page entry
page entry
page entry
page entry
Page directory
Page table
%cr3

## Slide 4: Previously
Problem
  One virtual memory access
  Requires two physical memory access
    Load directory entry
    Load page entry
  Generate “real” memory access
What a computer scientist do?
directory #
offset
Virtual Address
page #
page #
offset
Physical Address
directory entry
directory entry
directory entry
directory entry
page entry
page entry
page entry
page entry
Page directory
Page table
%cr3

## Slide 5: Previously
Problem
  One virtual memory access
  Requires two physical memory access
    Load directory entry
    Load page entry
  Generate “real” memory access
What a computer scientist do?
Add some cache!
directory #
offset
Virtual Address
page #
page #
offset
Physical Address
directory entry
directory entry
directory entry
directory entry
page entry
page entry
page entry
page entry
Page directory
Page table
%cr3

## Slide 6: Translation Lookaside Buffer (TLB)
Cache some PTE in hardware buffer
No need to go to physical memory to fetch PTE
Hardware memory is way faster than main memory!
We can also be clever about caching!

## Slide 7: Translation Lookaside Buffer (TLB)
Core
Core
TLB
TLB
L1 i-cache
L1 d-cache
L2 cache
L1 i-cache
L1 d-cache
L2 cache
L3 cache
RAM
Key/value store:
Key high bits of virtual address
Value is physical frame number

## Slide 8: Why does this work?
Program exhibit nice locality property
Temporal locality: when a process accesses virtual address x, it is likely to access it again in the future (e.g., variable on the stack)
Spatial locality: when a process accesses a virtual address x, the process is likely to address other addresses close to x (e.g., reading elements of an array on the heap)

## Slide 9: Memory lifecycle on x86
TLB hit?
TLB Look up
Access Ok?
Found PTE?
HW page fault
Calculate phys. address, send to L1/L2/L3/RAM
HW page fault
HW update TLB
HW walk page table
Check protection bits
Virtual address

## Slide 10: Memory lifecycle on x86
TLB hit?
TLB Look up
Access Ok?
Found PTE?
HW page fault
Calculate phys. address, send to L1/L2/L3/RAM
HW page fault
HW update TLB
HW walk page table
Check protection bits
Virtual address
Before raising fault, hardware set
register %cr2 to faulting address
and push error to stack:
Page not present in physical memory
Wrong access (e.g., writing on read only)

## Slide 11: Memory lifecycle on MIPS
TLB hit?
TLB Look up
Access Ok?
HW exception #1
read only fault
Calculate phys. address, send to L1/L2/L3/RAM
HW exception #2 or #3 TLB miss on load
miss on store
Check protection bits
Virtual address
Software logic

## Slide 12: TLB design trade-offs
Software TLB
  Good: freedom to design page directory, page tables and other structures as needed
  Good: OS can implement TLB eviction policies (i.e., deciding which entry to remove when full)
  Bad: slower than hardware
Hardware TLB
  Good: faster!
  Bad: OS cannot change the design of page directory, page table etc.